Fiber Optic Innovator

CWDM OADM Module (OADM)

| Features |  |
| --- | --- |
| Low insertion loss High channel isolation High stability and reliability |  |
| Application |  |
| CWDM system Metro/Access Networks CATV Fiberoptic System |  |

Specifications

| Type Parameter | 1ch | 2ch |
| --- | --- | --- |
| Channel Wavelength (nm) | 1471, 1491,..1551, 1571, 1591, 1611 |
| Channel space (nm) | 20 |
| Channel bandwidth (nm) | λc ± 6.5 |
| Add/Drop Channel Ripple (dB) | ≤0.4 |
| Insertion loss (dB) | Add/Drop Ch. | ≤0.7 | ≤1.0 |
|  | Express Ch. | ≤0.6 | ≤1.2 |
| Isolation (dB) | Drop | Adjacent Ch | ≥30 |
|  |  | Non-adjacent Ch | ≥40 |
|  | Add | Adjacent Ch | NA |
|  |  | Non-adjacent Ch | NA |
| Express Channel Isolation (dB ) | ≥25 |
| Directivity (dB) | ≥55 |
| Return loss (dB) | ≥50 |
| PDL (dB) | ≤0.15 |
| Wavelength thermal stability (nm/℃) | ≤0.003 |
| Insertion loss thermal stability (dB/℃) | ≤0.005 |
| Power handling (mW) | ≤500 |
| Operating temperature (℃) | 0 ~ +70 |
| Storage temperature (℃) | -40 ~ +85 |
| Dimensions (mm) | 80x60x10 or 100x80x10 |

Ordering Information:

| OADM | Type | Port Type | Wavelength | Pigtail Type | Fiber Type | Length | Connector |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | C=CWDM | 1=1ch 2=2ch | 1471=1471 1491=1291 …… 1611=1611 | 900=900um loose tube 2000=2mm loose tube 3000=3mm loose tube | 1=SMF-28e | 1= 1m X=Specif y | NE=None FA=FC/APC FC=FC/UPC SA=SC/APC SC=SC/UPC LC=LC/UPC LA=LC/APC XX=Other |

www.htopto.com