Fiber Optic Innovator

Coarse Wavelength Division Multiplexer Module (CWDM)

| Features |  |
| --- | --- |
| Low insertion loss High channel isolation High stability and reliability |  |
| Application |  |
| CWDM system Metro/Access Networks CATV Fiberoptic System |  |

Specifications

| Parameter | 4 Channel | 8 Channnel | 16 Channel |
| --- | --- | --- | --- |
| Central Wavelength(nm) | 1271, 1291, 1311, …..1551, 1571, 1591, 1611 |
| Channel space (nm) | 20 |
| Channel bandwidth (nm) | λc ± 6.5 |
| Channel flatness (dB) | ≤0.4 |
| Insertion Loss (dB) Max | ≤2.0 | ≤3.0 | ≤5.0 |
| Demux Isolation (dB) | Adjacent channel | ≥30 |
|  | Non-adjacent channel | ≥40 |
| Mux Isolation (dB) | Adjacent channel | ≥15 |
|  | Non-adjacent channel | ≥15 |
| Channel uniformity（dB） | ≤1.0 |
| Directivity (dB) | ≥55 |
| Return loss (dB) | ≥50 |
| PDL (dB) | ≤0.15 | ≤0.20 |
| Wavelength thermal stability (nm/℃) | ≤0.003 |
| Insertion loss thermal stability (dB/℃) | ≤0.005 |
| Power handling (mW) | ≤500 |
| Operating temperature (℃) | 0 ~ +70 |
| Storage temperature (℃) | -40 ~ +85 |
| Dimensions (LxWxH) (mm) | 100x80x10(ABS) | 141x115x18(ABS) |
|  | 110x95x7.5(Metal) |  |

Ordering Information:

| CWDM | Type | Port Type | Wavelength | Pigtail Type | Fiber Type | Length | Connector |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | M=Mux D=Demux | 4=4ch 8=8ch 16=16ch | 1271=1271 1291=1291 …… 1611=1611 | 900=900um loose tube 2000=2mm loose tube 3000=3mm loose tube | 1=SMF-28e | 1= 1m X=Specify | NE=None FA=FC/APC FC=FC/UPC SA=SC/APC SC=SC/UPC LC=LC/UPC LA=LC/APC XX=Other |

www.htopto.com